# System of N particles

Total mass:
M = sum from{i} m_{i}

Total linear momentum:
vec p = sum from{i} m_{i} vec v_{i}

Total angular momentum:
vec l = sum from{i} m_{i} vec r_{i} times vec v_{i}

Change of coordinates:

vec r_{i} = vec R + {vec r_{i}}^{'}
vec v_{i} = vec V + {vec v_{i}}^{'} V is the velocity of point R (relative to the origin), vi is the velocity of ri (relative to R)
vec p = sum from{i} m_{i} (vec V + {vec v_{i}}^{'}) ~=~ M vec V + sum from{i} m_{i} {vec v_{i}}^{'} ~=~ vec P + {vec p}^{'}

vec l = sum from{i} m_{i} vec r_{i} times vec v_{i} ~=~ sum from{i} m_{i} (vec R + {vec r_{i}}^{'}) times (vec V + {vec v_{i}}^{'}) ~=~ sum from{i} m_{i} vec R times vec V + m_{i} {vec r_{i}}^{'} times vec V + m_{i} vec R times {vec v_{i}}^{'} + m_{i} {vec r_{i}}^{'} times {vec v_{i}}^{'} ~=~ newline ~=~ M vec R times vec V `+` {sum from {i} m_{i} {vec r_{i}}^{'}} times vec V `+` vec R times {sum from{i} m_{i} {vec v_{i}}^{'}} `+` sum from {i} m_{i} {vec r_{i}}^{'} times {vec v_{i}}^{'} ~=~ newline ~=~ M vec R times vec V `+` (sum from {i} m_{i} {vec r_{i}}^{'}) times vec V `+` vec R times (sum from{i} m_{i} {vec v_{i}}^{'}) `+` sum from {i} m_{i} {vec r_{i}}^{'} times {vec v_{i}}^{'}

Center of mass:

vec R_{c} = {sum from{i} m_{i} vec r_{i}} over M = {sum from{i} m_{i} (vec R + {vec r_{i}}^{'})} over M = vec R + {sum from{i} m_{i} {vec r_{i}}^{'}} over M
If vec R = vec R_{c} then:

{sum from{i} m_{i} {vec r_{i}}^{'}} over M = 0 dlrarrow {sum from{i} m_{i} {vec r_{i}}^{'}} = 0

Angular/linear velocity:
vec v ~=~ {vec v}_{v parallel r} + {vec v}_{v ortho r} ~=~ {vec v}_{linear}+{vec v}_{angular} ~=~ {vec v}_{linear}+vec %alpha times vec r
angular velocity is perpendicular to the position (only changes direction of r)

With this definition, angular momentum becomes simply:

vec L = m vec r times vec v = m (vec r times {vec v}_linear + vec r times vec %alpha times vec r) = m (0 + vec r times vec %alpha times vec r) = m vec r times vec %alpha times vec r
# Cross product matrix definition

vec %alpha times vec r = left [ matrix { 0 # -%alpha_z # %alpha_y ## %alpha_z # 0 # -%alpha_x ## -%alpha_y # %alpha_x # 0 } right ] left [ matrix { r_x ## r_y ## r_z } right ]

# Rotation matrix definition

R = left [ matrix { 1 # 2 # 3 ## 2 # 3 # 4 ## 4 # 6 # 7 } right] newline det R = 1 newline R^-1=R^T

Robot:

A series of links/joints which condition motion

For each link there is a different basis. The basis for link N is aligned with the position of link N – 1.

So going from Link N – 1 to Link N we do a change of basis using a homogeneous transformation described by a 4x4 matrix, containing a pure rotation + pure translation:
T_{(i, i - 1)} = left [ matrix{ 1 # 2 # 4 # d_x ## 3 # 1 # 5 # d_y ## 7 # 8 # 1 # d_z ## 0 # 0 # 0 # 1 } right ]

{vec r_i}^{'} in local coordinates of frame i
{vec r}_i = T_{i-1} {{vec r}_i}^{'} in global coordinates (frame 0)

T_n = prod from{i=0} to{n-1} T_{(i, i - 1)}

The velocity in each basis and for a given point is represented also as a 4x4 matrix containing the angular velocity + linear velocity:
vec v = {vec v}_{linear}+vec %alpha times vec r = left [ matrix { 0 # -%alpha_z # %alpha_y # v_x ## %alpha_z # 0 # -%alpha_x # v_y ## -%alpha_y # %alpha_x # 0 # v_z ## 0 # 0 # 0 # 0 } right ] left [ matrix { r_x ## r_y ## r_z ## 1 } right ] = V_i {vec r}_i

vec r = vec r + vec v t= vec r + V_{i} vec r t= vec r (I + V_{i} t)

Velocity transforms as a regular vector:
v_n' in local coordinates
v_n in global coordinates = T_n-1 v'

But this is not the total velocity, just the velocity relative to this frame in global coordinates. For the total velocity we need to sum with the velocity of the reference frame, expressed also in the same global coordinates...

Global coordinates => inertial frame
Tab => transformation matrix

vec r = {vec r}_{ab} + {vec r}_{bc} + {vec r}_{cd} newline vec r drarrow "position vector" newline {vec r}_{ab} drarrow "relative position of basis B" newline {vec r}_{bc} drarrow "relative position of basis C" newline {vec r}_{cd} drarrow "relative position in basis C" newline
The global position is the sum of all the relative positions.

{d vec r} over {dt} = {d vec r_{ab}} over {dt} + {d vec r_{bc}} over {dt} + {d vec r_{cd}} over {dt} newline vec r_{bc} = sum from i {r_{c}}_{i} times {vec u}_{bi} newline {d vec r_{bc}} over {dt} = sum from i {{d r_{ci}} over {dt}} times {vec u}_{bi} + sum from i {{r}_{ci} times {{d vec u_{bi}} over {dt}}} newline

The global velocity is the sum of all the relative velocities.
Writing each relative vector in local coordinates times the local basis unit vectors, the relative velocity has two components: the local velocity + the velocity of the frame unit vectors

{d vec u_{ci}} over dt = {d {sum from j u_{bij} times vec u_{bj}}} over {dt}
Unit vectors of basic C, expressed in B basis coordinates
If the unit vectors are not expressed in global coordinates (where u_bi are constant), again we get the derivative of a product, and two velocities components...

{vec v}_{total} = {vec v}_0 + T_0 {vec v}_1 + dotslow + T_{i - 2}{vec v}_{i - 1} + T_{i - 1}{vec v}_i = T_{i - 2}V_{i - 1} + T_{i - 1}V_i {vec r}_i
Angular momentum:

{vec l}_{total} = ({vec v}_0 + T_0 {vec v}_1) times T_0 {vec r}_1 = {vec v}_0 times T_0 {vec r}_1 + T_0 {vec v}_1 times T_0 {vec r}_1 = V_0 T_0

# Basis

det A = 1 drarrow A^-1=A^T
(AB)^{-1} = B^{-1}A^{-1}
Three different basis A, B, C, three different basis transformations:
T_{AB} A = B newline T_{BC} B = C newline T_{BC} T_{AB} A = C
each column of A, B, C contains the coordinates of the basis unit vectors (in the original basis coordinates).
## Vector change of basis
Av_{a} = Bv_{b}
A and B are expressed in the default basis coordinates. v_a and v_b are the same vector expressed in the respective basis.
B^{-1}Av_{a} = v_{b} newline v_{a} = A^{-1}Bv_{b}

A = left [ matrix { 1 # 0 # 0 ## 0 # 1 # 0 ## 0 # 0 # 1 } right ] newline B = left [ matrix { 0 # 0 # 1 ## 1 # 0 # 0 ## 0 # 1 # 0 } right ] newline C = left [ matrix { 0 # 1 # 0 ## 0 # 0 # 1 ## 1 # 0 # 0 } right ]

Given a vector v in A basis coordinates, it's coordinates in the original basis are:
A v = left [ matrix { 1 # 0 # 0 ## 0 # 1 # 0 ## 0 # 0 # 1 } right ] left [ matrix { 0 ## 0 ## 1 } right ] = left [ matrix { 0 ## 0 ## 1 } right ]

B v = left [ matrix { 0 # 0 # 1 ## 1 # 0 # 0 ## 0 # 1 # 0 } right ] left [ matrix { 0 ## 0 ## 1 } right ] = left [ matrix { 1 ## 0 ## 0 } right ]

B^{T} v = left [ matrix { 0 # 1 # 0 ## 0 # 0 # 1 ## 1 # 0 # 0 } right ] left [ matrix { 0 ## 0 ## 1 } right ] = left [ matrix { 0 ## 1 ## 0 } right ]

## Transformation matrix change of basis:
T_{a} v_{a} = v^{'}_{a} dlrarrow T_{b} v_{b} = v^{'}_{b} newline T_{a} A^{-1}Bv_{b} = A^{-1}Bv^{'}_{b} dlrarrow T_{b} v_{b} = v^{'}_{b} newline B^{-1}AT_{a} A^{-1}Bv_{b} = v^{'}_{b} dlrarrow T_{b} v_{b} = v^{'}_{b} newline B^{-1}AT_{a} A^{-1}B=T_{b} newline newline v_{a} drarrow "coordinates of vector" vec v "in basis A" newline {v_{a}}^{'} drarrow "coordinates of vector" {vec v}^{'} "in basis A" newline v_{b} drarrow "coordinates of vector" vec v "in basis B" newline {v_{b}}^{'} drarrow "coordinates of vector" {vec v}^{'} "in basis B" newline T_{a} drarrow "transformation matrix" T "in basis A" newline T_{b} drarrow "transformation matrix" T "in basis B" newline

The transformation matrix components are given by the inner product of the new unit vectors and the old:
T_{BC} B = C dlrarrow T_{BC} = C B^{-1} = C B^{T} = left [ matrix { 0 # 1 # 0 ## 0 # 0 # 1 ## 1 # 0 # 0 } right ] left [ matrix { 0 # 1 # 0 ## 0 # 0 # 1 ## 1 # 0 # 0 } right ] = left [ matrix { 0 # 0 # 1 ## 1 # 0 # 0 ## 0 # 1 # 0 } right ]

left [ matrix { 0 # 0 # 1 ## 1 # 0 # 0 ## 0 # 1 # 0 } right ] left [ matrix { 0 # 0 # 1 ## 1 # 0 # 0 ## 0 # 1 # 0 } right ] = left [ matrix { 0 # 1 # 0 ## 0 # 0 # 1 ## 1 # 0 # 0 } right ]